## Slide 1
Fault Injection Attacks and Countermeasures
on TinyML Algorithms
Anthony Etim1*, Srilalith Nampally3*, Aubtin Rasouli3, Dustin Mazza3, Krishna Chilakapati3, Tinghung Chiu3, Ferhat Erata1,
Leyla Nazhandali3, Wenjie Xiong3 and Jakub Szefer2
Computer Architecture
and Security Lab (CASLAB)
1
2
3
*Anthony Etim and Srilaith Nampally contributed equally to this work.

## Slide 2
Tiny Machine Learning (TinyML)
• Runs ML inference directly on resource-constrained devices (microcontrollers, IoT nodes).
• Why: low latency, bandwidth savings, on-device privacy.
• Enabled by quantization, pruning, compact architectures (e.g., int8 with TensorFlow Lite and CMSIS-NN).
• Often deployed in the field — physically accessible to attackers.
Where TinyML lives
Microcontrollers
IoT sensors
Robots / drones
Wearables
©Anthony Etim
https://anthonyedemetim.com/
2

## Slide 3
Fault Injection Attacks
• Deliberate transient perturbations of computation or control flow.
• Common techniques: voltage glitching, EM pulses, clock glitches, lasers.
• Extensively studied for cryptographic implementations — but TinyML is largely unexplored.
• Goal: find stealthy faults — non-reset, attacker-controllable.
Fault Mechanisms in this Work
Mechanism | Effect
Voltage Glitch | VDD drop disrupts MCU computation
EM Pulse | Local transient currents corrupt state
Clock Glitch | Setup-time violations (out of scope)
Laser | Requires chip decapsulation
We focus on voltage glitching and EM injection — both practical for field attacks.
©Anthony Etim
https://anthonyedemetim.com/
3

## Slide 4
Threat Model
Adversary Capabilities
• Physical access to the device (IoT nodes, robots, edge sensors).
• Knows the TinyML model & firmware.
• Can inject voltage glitches or EM pulses synchronized with inference.
• Controls glitch timing, duration, voltage / pulse amplitude.
Out of Scope
• Modifying or retraining the model.
• Adversarial inputs.
• Rowhammer (needs code execution on device).
• Chip decapsulation / laser injection.
★ Example scenario: an outdoor motion-detection IoT node — injected faults can suppress true alerts or induce false alarms.
©Anthony Etim
https://anthonyedemetim.com/
4
• Tampering with encrypted input streams.

## Slide 5
Contributions and Take-aways
1
Systematic fault injection on TinyML
First evaluation across 4 TinyML models (FastGRNN, TinyCNN, Logistic Reg., Wake Word) under voltage glitching and EM injection on two MCU platforms.
2
Stealthy, attacker-controlled faults
Carefully tuned glitches force fixed-label outputs (e.g., TinyCNN → 9.7%) — not just random errors. EM produces persistent state corruption at certain probe positions.
3
Intermediate-value fault analysis
Recording layer outputs reveals: corruption is common, but only early-ROI bit-flips on wide spans of activations actually flip the final argmax.
4
RSR-based protections
Randomized self-reduction + median voting recovers baseline accuracy (< 1% drop) at modest overhead — 1.6× to 34× depending on model structure.
Code & artifacts: github.com/caslab-code/ml-fault-attacks-on-tinyml
©Anthony Etim
https://anthonyedemetim.com/
5

## Slide 6
Today's Talk
1
Motivation
TinyML &
Fault Injection
2
Attack Setup
Voltage glitch
and EM Fault Injection
3
Results
4 TinyML models
2 platforms
4
Defense (RSR)
Randomized
Self-Reduction
We show small, well-timed faults can controllably misclassify TinyML models, and propose RSR-based protections that recover accuracy with modest overhead.
©Anthony Etim
https://anthonyedemetim.com/
6

## Slide 7
Evaluation
Methodology
©Anthony Etim
https://anthonyedemetim.com/
7

## Slide 8
Four Target TinyML Models
FastGRNN
Domain
Tabular / Sequence
Architecture
Recurrent + FC
Dataset
MNIST-like 16×16
Attack Region of Interest (ROI)
First recurrent layer
Total Layers
2 layers
TinyCNN
Domain
Vision
Architecture
Conv → Pool → FC
Dataset
MNIST 8×8 (int8)
Attack Region of Interest (ROI)
First convolution
Total Layers
3 layers
Logistic Reg.
Domain
Binary classify
Architecture
FC + Sigmoid
Dataset
Tabular (11 feat.)
Attack Region of Interest (ROI)
Inner product
Total Layers
1 layer
Wake Word
Domain
Audio (always-on)
Architecture
3× FC + Softmax
Dataset
MFCC features (int8)
Attack Region of Interest (ROI)
First dense layer
Total Layers
4 layers
Spans float & int8 inference, matrix-vector / matrix-matrix / convolution kernels, and different control-flow patterns.
©Anthony Etim
https://anthonyedemetim.com/
8

## Slide 9
Hardware Setup
©Anthony Etim
https://anthonyedemetim.com/
9
Husky
SAMS4S Board
Riscure Glitcher
Riscure Spider
Notes: Change to actual pictures of

## Slide 10
Hardware Setup
©Anthony Etim
https://anthonyedemetim.com/
10
(a)
Pinata Voltage Glitching
Spider VCC glitcher
STM32F417IG MCU
(b)
Pinata EM Fault Injection
EM probe and pulse generator
(c)
ChipWhisperer-Husky Voltage Glitching
Crowbar glitch on SAM4S
Each trial: Correct / Misprediction / Reset/Hang. We sweep glitch parameters within a Region of Interest (ROI) — typically the first compute-heavy layer.
Husky
SAMS4S Board
Riscure Glitcher
Riscure Spider
Notes: Change to actual pictures of

## Slide 11
Finding Effective (and Stealthy) Faults
Two-stage parameter sweep: maximize mispredictions, minimize resets.
1
Strength × Duration × Position Sweep
• Pinata voltage: VDD target × glitch duration
• Pinata EM: pulse amplitude × probe position
• ChipWhisperer: Optuna search over {width, repeat, offset, ext_offset}
• Pick op points that max mispredictions under a reset-rate cap.
2
Injection-Time Sweep
• Sweep normalized injection time t ∈ [0, 1] across the ROI.
• t = 0 → ROI entry, t = 1 → ROI exit.
• Allows cross-model and cross-platform comparison even when ROI runtimes differ.
• Goal: find the most reliable non-reset faults.
©Anthony Etim
https://anthonyedemetim.com/
11

## Slide 12
Experimental
Results
©Anthony Etim
https://anthonyedemetim.com/
12

## Slide 13
Pinata Voltage Glitching — All Four Models
Confusion matrices at the most-effective injection time per model.
©Anthony Etim
https://anthonyedemetim.com/
13

## Slide 14
Pinata Voltage Glitching — All Four Models
Confusion matrices at the most-effective injection time per model.
FastGRNN
TinyCNN
Logistic Reg.
Wake Word
©Anthony Etim
https://anthonyedemetim.com/
14
Baseline | t = 0.6t | t = 0t
98.83% | 93.33% | 15.38%
Baseline | t = 0.12t | t = 0t
99.07% | 68.75% | 9.71%
Baseline | t = 0.9t
85.19% | 77.85%
Baseline | t = 0.5t
87.38% | 81.10%
Notes: More work needs to be done to find oput why fast tgrnn is robust

## Slide 15
ChipWhisperer-Husky — Cross-Platform Confirmation
Same fault model, different MCU (SAM4S, Cortex-M4) — confirms attack generalizes.
TinyCNN is most vulnerable
62.24% accuracy with bias toward labels {3, 7, 9}; very early timings push reset rate to 63%.
Output collapse on binary models
Logistic Reg. predicts class 1 for nearly all inputs (56.32%); Wake Word collapses to class 0.
FastGRNN is the most robust
93.86% accuracy under attack — modest but consistent degradation only.
©Anthony Etim
https://anthonyedemetim.com/
15

## Slide 16
EM Fault Injection — Spatial Sensitivity
Probe Position 1 — TinyCNN
• Isolated, prediction-specific faults.
• At t = 0: accuracy drops to 55.9% (often mispredicts label “7”).
• At t = 0.1: recovers to 94.12% — narrow attack window.
Probe Position 2 (millimeters away)
• Persistent state corruption.
• When a fault hits, all subsequent predictions are corrupted until power-cycle.
• Compatible with corruption of registers / SRAM.
• Intermittent and not repeatable — high impact, low controllability.
Takeaway: EM fault injection is highly spatially sensitive — millimeters change the failure mode entirely.
©Anthony Etim
https://anthonyedemetim.com/
16

## Slide 17
Why Do Some Faults Misclassify and Others Don't?
TinyCNN — recording layer outputs under voltage glitching:
1
Intermediate corruption is common
Whenever the device survives the glitch, layer outputs differ from baseline — most of the time.
2
Early faults spread widely
Early within ROI, a glitch corrupts values that still feed many downstream MAC operations — a single fault contaminates a wide span of bytes, more likely to flip the final argmax.
3
Late faults (conv layer) get masked
Late within ROI, most of the layer's output is already committed — corruption is overwhelmed by classifier margin.
©Anthony Etim
https://anthonyedemetim.com/
17
Notes: Is t here the whole network or the convolution layer? -> Conv layer -> check with Sri?
Ask why fastgrnn is better -> more work needs to be done
Clarify if what t means

## Slide 18
Bit-Level Effects in TinyCNN Convolution Output
Avg. Hamming Weight for Intermediate values vs. injection time t
Two patterns to notice:
• The earliest affected bytes shift right as t grows — faults land on different dynamic instruction windows.
• Broader, denser bit-flip regions co-occur with higher effective error (cf. previous slide).
Why early-ROI matters
Conv output (288 B) feeds many downstream MAC ops → early corruption contaminates a wide span of activations and is more likely to flip the final argmax.
©Anthony Etim
https://anthonyedemetim.com/
18

## Slide 19
Key Observations — Voltage vs. EM, Across Models
Timing matters
Effective faults concentrated in early-ROI windows. At t ≈ 0, faults often land on init/UART code — but still produce repeatable, attacker-useful failures.
©Anthony Etim
https://anthonyedemetim.com/
19

## Slide 20
Key Observations — Voltage vs. EM, Across Models
Timing matters
Effective faults concentrated in early-ROI windows. At t ≈ 0, faults often land on init/UART code — but still produce repeatable, attacker-useful failures.
Model structure matters
TinyCNN is most vulnerable (predictable single-class failures < 20% acc.). FastGRNN is most robust. Logistic Reg. & Wake Word in between (6–8% drops, output collapse risk).
©Anthony Etim
https://anthonyedemetim.com/
20

## Slide 21
Key Observations — Voltage vs. EM, Across Models
Timing matters
Effective faults concentrated in early-ROI windows. At t ≈ 0, faults often land on init/UART code — but still produce repeatable, attacker-useful failures.
Model structure matters
TinyCNN is most vulnerable (predictable single-class failures < 20% acc.). FastGRNN is most robust. Logistic Reg. & Wake Word in between (6–8% drops, output collapse risk).
Voltage > EM for control
Voltage glitching: easy to parameterize, reproducible, fewer resets. EM injection: more spatially/mechanically sensitive, but reaches modes voltage cannot (persistent corruption).
©Anthony Etim
https://anthonyedemetim.com/
21

## Slide 22
Key Observations — Voltage vs. EM, Across Models
Timing matters
Effective faults concentrated in early-ROI windows. At t ≈ 0, faults often land on init/UART code — but still produce repeatable, attacker-useful failures.
Model structure matters
TinyCNN is most vulnerable (predictable single-class failures < 20% acc.). FastGRNN is most robust. Logistic Reg. & Wake Word in between (6–8% drops, output collapse risk).
Voltage > EM for control
Voltage glitching: easy to parameterize, reproducible, fewer resets. EM injection: more spatially/mechanically sensitive, but reaches modes voltage cannot (persistent corruption).
End-to-end ≠ internal
Confusion matrices alone can't separate masked corruption from real misprediction. Recording intermediate values is essential to understand what's happening.
Synthesis: Carefully tuned faults can controllably force fixed-label outputs — not just random errors. We need protections.
©Anthony Etim
https://anthonyedemetim.com/
22

## Slide 23
Lessons Learned — Generalizing to Other Algorithms
t = 0 hits firmware, not the model
Glitches at t ≈ 0 reliably crash accuracy, but they hit UART / firmware setup — not the ML kernel. Report per-region breakdowns or I/O bugs masquerade as ML vulnerability.
©Anthony Etim
https://anthonyedemetim.com/
23

## Slide 24
Lessons Learned — Generalizing to Other Algorithms
t = 0 hits firmware, not the model
Glitches at t ≈ 0 reliably crash accuracy, but they hit UART / firmware setup — not the ML kernel. Report per-region breakdowns or I/O bugs masquerade as ML vulnerability.
Use Bayesian search (Optuna)
Brute-force sweeping the 4-D glitch space (width × offset × ext_offset × repeat) takes days per platform. Optuna-style Bayesian search finds productive operating points in hours.
©Anthony Etim
https://anthonyedemetim.com/
24

## Slide 25
Lessons Learned — Generalizing to Other Algorithms
t = 0 hits firmware, not the model
Glitches at t ≈ 0 reliably crash accuracy, but they hit UART / firmware setup — not the ML kernel. Report per-region breakdowns or I/O bugs masquerade as ML vulnerability.
Use Bayesian search (Optuna)
Brute-force sweeping the 4-D glitch space (width × offset × ext_offset × repeat) takes days per platform. Optuna-style Bayesian search finds productive operating points in hours.
Inject early in the ROI
Across all four models, effective errors cluster in the first ~10–20% of the ROI — a single early-cycle fault contaminates many downstream MAC ops. Target the first compute-heavy layer.
©Anthony Etim
https://anthonyedemetim.com/
25

## Slide 26
Lessons Learned — Generalizing to Other Algorithms
t = 0 hits firmware, not the model
Glitches at t ≈ 0 reliably crash accuracy, but they hit UART / firmware setup — not the ML kernel. Report per-region breakdowns or I/O bugs masquerade as ML vulnerability.
Use Bayesian search (Optuna)
Brute-force sweeping the 4-D glitch space (width × offset × ext_offset × repeat) takes days per platform. Optuna-style Bayesian search finds productive operating points in hours.
Inject early in the ROI
Across all four models, effective errors cluster in the first ~10–20% of the ROI — a single early-cycle fault contaminates many downstream MAC ops. Target the first compute-heavy layer.
Log intermediate values
End-to-end accuracy conflates “fault was masked” with “no fault occurred.” Per-layer logging reveals true intermediate-value error rates and where corruption propagates.
Bottom line: These methodology lessons generalize across algorithms — set up Optuna, log internals, target early-ROI cycles. The rest is model-specific tuning.
©Anthony Etim
https://anthonyedemetim.com/
26

## Slide 27
Defense:
Randomized Self-Reduction
©Anthony Etim
https://anthonyedemetim.com/
27

## Slide 28
Randomized Self-Reduction (RSR) — The Idea
• Idea: compute f(x) by evaluating f on a few random inputs and recombining the results.
• Toy example (linear function f(x) = c·x):
• pick random r → f(x) = c·(x-r) + c·r
= f(x − r) + f(r).
• Repeat T times with fresh randomness, then take the median — outliers from faults are filtered out.
RSR Pipeline
Input x
Randomize
x → x+r, r
Evaluate f
on each variant
Recombine
(median vote)
Output f(x)
©Anthony Etim
https://anthonyedemetim.com/
28
Notes: so a single evaluation on x is replaced by two evaluations on
random points x − r and r and one addition

## Slide 29
Protecting Logistic Regression
Two RSR identities
1. Inner product is linear:
wᵀ(x + r) − wᵀr = wᵀx
2. Sigmoid has a multiplicative RSR:
σ(a − b) = σ(a)·(1 − σ(b))
÷ [−2σ(a)σ(b) + σ(a) + σ(b)]
Recover σ(wᵀx + b) from σ(wᵀ(x+r)+b) and σ(wᵀr) — without ever computing the unprotected inner product.
Self-Correcting Logistic Regression
Repeat N times (N = ⌈log(1/β)⌉):
sample r ~ Uniform(−1, 1)ⁿ
p₁ ← σ(wᵀ(x+r) + b)
p₂ ← σ(wᵀr)
yᵢ ← rsrprop(p₁, p₂)
Return median(y₁ … y_N) as ŷ
Same fixed-point representation — drop-in replacement.
©Anthony Etim
https://anthonyedemetim.com/
29

## Slide 30
Matrix-Vector Multiply & Convolution
Both reduce to the same protected primitive — bilinearity does the work.
Matrix-Vector Multiplication
Decompose both operands:
v = v_rand + v_pert
W = W_rand + W_pert
Bilinearity → 4 partial products:
vW = v_r·W_r + v_p·W_r
+ v_r·W_p + v_p·W_p
Repeat T = 5 times with fresh randomness; elementwise median filters out faulted entries.
Convolution (via im2col)
Convolution = sequence of vector-matrix products:
Each spatial patch → flattened vector A
Each output channel → weight column B
Apply same RSR decomposition:
A = A_r + A_p, B = B_r + B_p
Reuses the protected vec-mat primitive — no architecture changes.
©Anthony Etim
https://anthonyedemetim.com/
30

## Slide 31
Protection: Effectiveness & Overhead
Accuracy: Baseline / Faulted / Protected
Model | Baseline | Faulted | Protected
FastGRNN | 98.83% | 15.4 – 98.8% | 98.75%
Logistic Reg. | 85.19% | 77.9 – 85.2% | 85.24%
Wake Word | 87.38% | 81.1 – 91.2% | 87.36%
TinyCNN | 99.07% | 9.7 – 98.4% | 98.80%
Protected accuracy < 1% drop from baseline across all 4 models.
Runtime Overhead
Chart: × over baseline
| TinyCNN | Wake Word | Logistic Reg. | FastGRNN
Overhead (×) | 1.6 | 2.5 | 6 | 34
FastGRNN's overhead reflects RSR cost compounding across recurrent timesteps.
Bottom line: RSR fully recovers accuracy under attack with overhead within typical embedded budgets for security-sensitive deployments.
©Anthony Etim
https://anthonyedemetim.com/
31
Notes: Backup slide for slide fastgrnn architecture ->

## Slide 32
Limitations & Future Directions
RSR protects transient computation faults
It does not guarantee recovery from persistent architectural state corruption (Probe Position 2 EM regime — corrupted SRAM/registers across inferences).
Persistent faults need complementary defenses
Canaries, checksums on model state, and periodic state-integrity checks remain necessary for full coverage.
Multiple MCU evaluation
Two MCU families covered (STM32 and SAM4S). Broader silicon (RISC-V, vendor-specific accelerators) and more complex TinyML models remain to be evaluated.
Beyond inference
On-device fine-tuning and federated TinyML create new attack surfaces our threat model does not yet address.
©Anthony Etim
https://anthonyedemetim.com/
32

## Slide 33
Summary
1
Systematic fault injection on TinyML
First evaluation across 4 TinyML models (FastGRNN, TinyCNN, Logistic Reg., Wake Word) under voltage glitching and EM injection on two MCU platforms.
2
3
4
©Anthony Etim
https://anthonyedemetim.com/
33

## Slide 34
Summary
1
Systematic fault injection on TinyML
First evaluation across 4 TinyML models (FastGRNN, TinyCNN, Logistic Reg., Wake Word) under voltage glitching and EM injection on two MCU platforms.
2
Stealthy, attacker-controlled faults
Carefully tuned glitches force fixed-label outputs (e.g., TinyCNN → 9.7%) — not just random errors. EM produces persistent state corruption at certain probe positions.
3
4
©Anthony Etim
https://anthonyedemetim.com/
34

## Slide 35
Summary
1
Systematic fault injection on TinyML
First evaluation across 4 TinyML models (FastGRNN, TinyCNN, Logistic Reg., Wake Word) under voltage glitching and EM injection on two MCU platforms.
2
Stealthy, attacker-controlled faults
Carefully tuned glitches force fixed-label outputs (e.g., TinyCNN → 9.7%) — not just random errors. EM produces persistent state corruption at certain probe positions.
3
Intermediate-value fault analysis
Recording layer outputs reveals: corruption is common, but only early-ROI bit-flips on wide spans of activations actually flip the final argmax.
4
©Anthony Etim
https://anthonyedemetim.com/
35

## Slide 36
Summary
1
Systematic fault injection on TinyML
First evaluation across 4 TinyML models (FastGRNN, TinyCNN, Logistic Reg., Wake Word) under voltage glitching and EM injection on two MCU platforms.
2
Stealthy, attacker-controlled faults
Carefully tuned glitches force fixed-label outputs (e.g., TinyCNN → 9.7%) — not just random errors. EM produces persistent state corruption at certain probe positions.
3
Intermediate-value fault analysis
Recording layer outputs reveals: corruption is common, but only early-ROI bit-flips on wide spans of activations actually flip the final argmax.
4
RSR-based protections
Randomized self-reduction + median voting recovers baseline accuracy (< 1% drop) at modest overhead — 1.6× to 34× depending on model structure.
Code & artifacts: github.com/caslab-code/ml-fault-attacks-on-tinyml
©Anthony Etim
https://anthonyedemetim.com/
36

## Slide 37
Fault Injection Attacks and Countermeasures
on TinyML Algorithms
Thank you!
Questions?
Code: github.com/caslab-code/ml-fault-attacks-on-tinyml
Supported by NSF (CCF-2245344, CCF-2153748, CNS-2442993), CCI, AFOSR (FA9550-22-1-0548).
©Anthony Etim
https://anthonyedemetim.com/
37
anthony.etim@yale.edu, nsrilalith@vt.edu, aubtinr@vt.edu

## Slide 38
Backup: Why FastGRNN Has the Highest Protection Overhead
Only the matVecs are protected — but they live inside the recurrent loop, so RSR cost is paid every timestep.
Protected FastGRNN Cell — Pseudocode
for t = 0 to T_steps−1: ← recurrent loop, T_steps = 16
normalize_input(x[t])
protectedmatVec(W1, x_norm) ← T=5 RSR variants + median
protectedmatVec(W2, ·) ← T=5 RSR variants + median
protectedmatVec(U1, h) ← T=5 RSR variants + median
protectedmatVec(U2, ·) ← T=5 RSR variants + median
for i = 0 to hiddenDims−1:
gate = sigmoid(z[i] + Bg[i]) (unprotected)
update = tanh (z[i] + Bh[i]) (unprotected)
h[i] = gate·h[i] + (ζ(1−gate)+ν)·update
Red = the only RSR-protected operations. The activations and hidden-state update are left untouched.
Why the Cost Compounds
matVec dominates the inference cost
Almost all FLOPs in the cell live in the four low-rank multiplies (W1, W2, U1, U2) — protecting them is enough to dominate the runtime.
Each protectedmatVec ≈ 4·T_rsr → ~20×
One matVec → 4 partial products × T=5 RSR repeats + elementwise median (T_steps cancels in the ratio).
Tight recurrent loop hurts amortization
4 small low-rank matVecs × 16 timesteps = 64 protected calls per inference. Per-call costs (RNG, median scan, buffer setup) don't amortize and push the ratio past the 20× per-call multiplier.
Net effect
~20× per call, plus per-call setup amplification → 34× measured. One-shot models: matVec is a smaller share of total inference, so net overhead is just 1.6–9×.
Bottom line: each protectedmatVec is ~20× a regular matVec, and FastGRNN spends nearly all of inference inside 4 × 16 = 64 such calls — small low-rank matVecs amplify per-call overhead to ~34×.
©Anthony Etim
https://anthonyedemetim.com/
38